## Slide 1: Quantifying the Design-Space Tradeoffs in Autonomous Drones
Ramyad Hadidi, Sam Jijina, Nima Shoghi, Bahar Asgari, Adriana Amyette, Hyesoon Kim
Accepted by Architectural Support for Programming Languages and Operating Systems
(ASPLOS ’21), April 19-23, 2021
Georgia Institute of Technology
Presenter: Gao Weiguo

## Slide 2
Over the last decade, significant progress has been made in the development of autonomous systems.
The quadcopter design possesses many advantages over other aerial vehicle designs in terms of simplicity and efficiency.
With fully autonomous flight capabilities coupled with user-specific applications, autonomous drones are widely used in urban planning ＆ mapping, agriculture, cinematography ＆ photography, rescue ＆ firefighting.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Autonomous Drones

## Slide 3
Autonomous drones are edge compute agents that must operate within constraints.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Drones are Unique
Operate under various local conditions
With limited energy and weight carrying
While executing a safe flight plan

## Slide 4
Despite huge technological advances in drones, these problems have been approached in isolation.
End-to-end design-space tradeoffs are largely unknown
(e.g.,how battery choice affects flight time)
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Research on Drones
We can quantify design-space tradeoffs to address right set of problems.

## Slide 5
To answer such questions and solve worthy research problems, we need to:
understand fundamental drone subsystems;
classify drone computations and their requirements;
extract design-space tradeoffs;
have access to a reproducible experimental platform.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Challenges of Quantifying

## Slide 6
Propulsion System
Use four identical motor-rotors, two pairs of which spin in opposite directions.
Power Delivery System
LiPo batteries have the highest energy density and discharge rate.
Control, Compute, and Acquisition System
A. Inner vs. Outer Loops:
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Fundamental Subsystems

## Slide 7
The inner-loop control manipulates the drone actuators to reach the target set points dictated by the outer-loop control.
B. Hardware-Software Stack:
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Fundamental Subsystems
The flight controller boards with additional on-board sensors directly manipulate ESCs(electronic speed controllers) and sensors.

## Slide 8
C. Inner-Loop Control:
In the inner loop, the control layer uses the on-board sensors to stabilize the drone and reach to target set points dedicated by the outer loop.
D. Inner-Loop Control Computations:
filter computations such as EKF for data fusion and updating proportional-integral-derivative(PID) controllers；
algebraic functions for state estimation such as air drag and trajectory.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Fundamental Subsystems

## Slide 9
Quantifying each tradeoff correlation with weight, which defines the order of power consumption in a drone.
Battery Stored Energy&Weight
Derived a linear relationship between the capacity and the weight of the batteries.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Quantifying Tradeoffs

## Slide 10
ESCs Current&Weight
The maximum continuous current have a linear relationship with the weight of ESCs.
Frames
The wheelbase is proportional to weight.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Quantifying Tradeoffs

## Slide 11
Propulsion System
Firstly, we set the maximum propeller diameter in inches dictated by the wheelbase.
Then, we extract the thrust and 𝐾𝑣 rating of the motors from data released by 150 manufacturers.
Finally, we calculate the minimum required max current draw per motor.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Quantifying Tradeoffs

## Slide 12
Flight Controllers, On-Board Computation, & Sensors
Basic: provides only necessary inner-loop functions with limited outer-loop capabilities.
Improved: provides customizable inner-loop functions and a few outer-loop functions.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Quantifying Tradeoffs

## Slide 13
How to?
For each frame, we choose the propeller with the maximum size, find the required RPM for the motors, and choose the best matching motor depending on the number of cells in the LiPo battery.
Then, from the maximum motor current draw, we choose ESCs.
By assuming a low-load hovering condition (20-30% of the maximum current draw) with 85% LiPo battery capacity limit, we calculated the power consumption.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Computation Footprint

## Slide 14
Develop and fly test a fully open-source experimental drone
Quantifying the Design-Space Tradeoffs in Autonomous Drones
A Reproducible Experimental Platform
ACM Artifact available for build guide and software stack
Access to autopilot code
Fully customizable across hardware-software stack
Ability to add new sensors or development boards
Up to 200g payload for new boards and sensors
Inexpensive compared to any commercialized platform

## Slide 15
Explore offloading ORB SLAM onto four hardware platforms.
(Rpi,TX2,FPGA,ASIC)
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Optimization Impact
Running Autopilot and SLAM on Rpi
SLAM in not only not fast enough, but also it negatively impacts the performance of the autopilot.
Thus, by offloading SLAM onto a low-power platform such as ASIC/FPGA, we can potentially save up to 2W, which would have a high impact for small drones.

## Slide 16
Explore offloading ORB SLAM onto four hardware platforms.
(Rpi,TX2,FPGA,ASIC)
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Optimization Impact
Offloading SLAM to Hardware Accelerators
improves the performance of SLAM;
helps extend the flight time by consuming less power;
preventing lags in the responses of the autopilot.

## Slide 17
Formalizing the fundamental drone subsystems and quantifying the design-space tradeoffs by studying 300 components.
Separating the required computing for inner- vs. outer-loop controls and their gained benefits.
Showcasing optimizations and its effect on flight time. (e.g., SLAM)
Releasing an open-source artifact containing a reproducible platform with a fully customizable hardware-software stack.
Quantifying the Design-Space Tradeoffs in Autonomous Drones
Contributions

## Slide 18
Thanks